## Slide 1
  Complex material datasets challenge mach-ine learning due to sparse features.
  Composition crucial: composition proporti-ons overlooked.
  Compositional features present: Atomic info missing.
  Image mapping: Using XenonPy expand 58 elemental points, 406 extended dimensions.
  Grayscale images for CNN extraction.
Enhancing Materials Property Prediction: A Multimodal Learning via Image Mapping of Material Compositions
Introduction
Densification and Prediction: Atomic features for 2D grayscale images; MCVN predicts steel properties, classifies amorphous alloys. [See Figure A]
  Expert-based visualization: Enhances compositional features in material ML tasks.
  Multimodal deep-network model: Integrates visualization images & raw features, improves accuracy. [See Figure B]
This approach enhances model performances on small sparse matrix samples by expanding material composition data, offering a universal paradigm for predicting material properties.
Feature Enhancement: Densifies sparse composition, boosts generalization.
Modal Translation: XenonPy, element-level features, multimodal grayscale dataset.
Multimodal Learning: MCVN enhances material property predictions.
Modal Translation
Results
Conclusion
Figure A. Better utilization of composition for material property prediction using the MCVN.
Figure B. Material composition visualization network architecture.
Yu Yeyong a, Wu Xing a,c, Zhang Huirana,c , Qian Quan a, b, c,*
a. School of Computer Engineering and Science, Shanghai University
b. Materials Genome Institute, Shanghai University, Shanghai
c. Zhejiang Laboratory, Hangzhou
International Workshop on Data-driven Computational and Theoretical Materials Design (DCTMD)
“ Unlocking the AI Future of Materials Science ”
Methods
Self-attention Mechanism: Reduces external info reliance, captures internal relevance effectively.
Process Flow: Feature Enhancement with Xenonpy.
Arrangement: Template of compositional features.
Grayscale Image: Element-level description of features
Classification Task
Unbalanced amorphous alloy dataset: Increased avg. 𝑅𝑒𝑐𝑎𝑙𝑙 (CRA small-class) from 0.58 to 0.78.
NIMS's steel dataset: 4% 𝑅² improvement (0.92 avg. 𝑅²)
SRIM's steel dataset: 𝑅² = 0.835 on EL (vs 0.64 avg. 𝑅²).
Regression Task
Reference
Better utilization of materials’ compositions for predicting their properties: Material composition visualization network[J]. Engineering Applications of Artificial Intelligence
FTAP: Feature transferring autonomous machine learning pipeline[J]. Information Sciences
Email: qqian@shu.edu.cn
Organizer
Materials Genome Institute, Shanghai University
Shanghai, China October 9-13, 2024
Partners and Sponsors